## Slide 1: Assembly of the IAS
Dr. Mahmoud Obaid
Nov 2020

## Slide 2: Calculate z= (a-b)*c
To calculate z = (a –b) * c
First of all you need to assign memory locations to the variables:
Assume a is in memory location 300
a | M(300)
b | M(301)
c | M(302)
z | M(303)

## Slide 3: Now the instructions
Suppose you start your program from Memory location 100
The first step is to load the AC with the variable a
  LOAD M(300)
Next you subtract
  SUB M(301)
At this point we have a – b stored in the AC

## Slide 4: The multiplication
In order to multiply you need to load MQ with a value then Multiply it by a value in memory.
We need to multiply what is stored in the AC with the value c
But before we do I will store the value in the AC in another memory location? What value does it hold?
STOR M(305)
Now load MQ with c
  LOAD MQ, M(302)
Now multiply it with Memory location 305? Why?
  MULT M(305)

## Slide 5: Storing the multiplication result
The result of multiplication is stored in AC,MQ
So you need to store both in this way
  STOR M(303)
  LOAD MQ
  STOR M(304)
  QUESTIONS?

## Slide 6: The final program
Memory location | Left instruction | Right instruction
100 | LOAD M(300) | SUB M(301)
101 | STOR M(305) | LOAD MQ, M(302)
102 | MULT M(305) | STOR M(303)
103 | LOAD MQ | STOR M(304)
104 | HALT |